The detailed specification of the Scope Corder is as follows:

Item 1:

High-Voltage 100 kS/s 16-Bit Isolation Module

Input channels 2

Input couplings AC, DC, GND, AC-RMS, DC-RMS

Maximum sampling rate 100 kS/s

A/D conversion resolution 16 bits (2400 LSB/div)

Input type Isolated unbalanced

DC, up to 40 kHz

RMS measurement mode DC, 40 Hz to 10 kHz

Input range (10:1) 200 mV/div to 2000 V/div (in steps of 1, 2, or 5)

DC offset ±5 div

DC accuracy (RMS measurement mode)

±(1.0% of 10 div)

AC accuracy (RMS measurement mode)1

Sine wave input ±(1.5% of 10 div)

Input impedance 1 MΩ ± 1%, approx. 35 pF

Connector type Isolated type BNC connector