- DIGITAL BENCH TEMPERATURE INDICATOR

For use with type K and type J thermocouples

Miniature sockets to connect input from selector switch

Range		: -50 to 1200(C

Accuracy		: ( 0.2% of reading

Resolution		: ( 150(C  -  0.1(C ;  ( 150(C  -  1(C

Display		: 3½  digits, LED

Cold Junction	: automatic

Power supply	: 220 V / 50 Hz

Sensor input	: miniature thermocouple connector

Calibration certificates, traceable to National / International standards.